|  | The right container for every product Hapag-Lloyd offers you a wide range of standard and special containers, which enables us to provide you with a suitable container for every product. It goes without saying that the containers we supply meet all ISO requirements. The regular inspection intervals and repair procedures for containers are monitored and approved by the German authorities in accordance with international guidelines (CSC/ACEP). The procedure is regularly supervised and confirmed by a certification society. (ISO 9002) Looking for a special solution for transporting your goods? Just phone your nearest Hapag-Lloyd office. We will be glad to assist you. Containergroups General view of all Container-Types Standard-Container Refrigerated-Container-Types Special-Container |
| --- | --- |

|  | Container-Types General view In this page you can get an overview over all Hapag-Lloyd Container Types. |  |
| --- | --- | --- |
|  | Standard-Container 20' 40' 40' High-Cube Version Suitable for any general cargo. Various lashing devices on the top and bottom longitudinal rails and cornerpost. Hardtop-Container 20' 40' 40' High-Cube Version Equiped with a removable steelroof. Especially for heavy loads and overheight cargo. Loading through roof opening and doorway by swung out doorheader. Open-Top-Container 20' 40' With removable tarpaulin. Especially for overheight cargo. Loading either from top side or door side by swung out doorheader. Flat rack 20' 40' 40' High-Cube Version Especially for heavy loads and overwidth cargo. Platform 20' 40' Especially for heavy loads and oversized cargo. Non domestic shipments. Ventilated-Container 20' Especially for cargo which needs ventilation. Refrigerated-Container 20' 40' High-Cube Version 40' Reefer Container do have their own electrically operated cooling/ heating unit. The power supply is provided by ship's electrical plant, by terminal or by "clip-on" diesel generator. Tank-Container 20' For the transport of liquid food, e.g.: - Alcohols - Fruit juices - Edible oils - Food additives. Hapag-Lloyd offers you, with regard to your requirements a made to measures service. For more details please contact your nearest Hapag-Lloyd office or agent. |

|  | Standard-Container 20' |  |
| --- | --- | --- |
|  | Millimeter/mm Foot/ft Kilogram/kg Lbs/Pound Internal Length 5895 19' 4 1/8" Weight Max. Gross 30480 67200 Width 2350 7' 8 1/2" Tare 2250 4960 Height 2392 7' 10 1/8" Max. Payload 28230 62240 Door Width 2340 7' 8 1/8 " Opening Cubic meter/m³ Cubic foot/cu.ft Height 2292 7' 6 1/4 " Capacity 33,2 1172 ISO-Code ISO Type Group ISO Size Type 22 GP 22 G1 |

|  | Standard-Container 40' |  |
| --- | --- | --- |
|  | Millimeter/mm Foot/ft Kilogram/kg Lbs/Pound Internal Length 12029 39' 5 1/2" Weight Max. Gross 30480 67200 Width 2350 7' 8 1/2" Tare 3780 8330 Height 2392 7' 10 1/8" Max. Payload 26700 58870 Door Width 2340 7' 8 1/2" Opening Cubic meter/m³ Cubic foot/cu.ft Height 2292 7' 6 1/4" Capacity 67,7 2390 ISO-Code ISO Type Group ISO Size Type 42 GP 42 G1 |

|  | Standard-Container 40' High-Cube |  |
| --- | --- | --- |
|  | Millimeter/mm Foot/ft Kilogram/kg Lbs/Pound Internal Length 12024 39' 5 3/8" Weight Max. Gross 30480 67200 Width 2350 7' 8 1/2" Tare 4020 8860 Height 2697 8' 10 1/8" Max. Payload 26460 58340 Door Width 2338 7' 8" Opening Cubic meter/m³ Cubic foot/cu.ft Height 2585 8' 5 3/4" Capacity 76,3 2694 ISO-Code ISO Type Group ISO Size Type 45 GP 45 G1 |